BLUE CRAB CAN SEAM EVALUATION RECORD

FOR 401x301 Tinplate, Aluminum Ends

Company Name:    Glorious Crab, Inc.*     	Address:    123 Harvest Way, Seaside, MD 12345*  	     Person Responsible: Packing Room Supervisor*

Critical Limits: 	Visual acceptable			Frequency:	 Conduct a complete evaluation at start-up and after adjustments.

Thickness .060±.002 	 Visual check, every batch.

Overlap .045 or longer, where Overlap = CH + BH + .012 - L

Tightness 80-100%

| Date | Time | Code | Visual Accept/ Reject | Thickness .060(.002 | Length (L) .125 maximum | Body-hook (BH) .080(.008 | Cover-hook (CH) .080(.008 | Overlap .045 minimum | Tightness 80-100% | Pressure/ Vacuum Accept/ Reject | Operator’s Initials |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Comments: |

Reviewer_______________________________	         Date___________		Reviewer_______________________________	         Date___________

*NOTE:  	This generic record is for your information only. It should not be used without

modification. Each record must be specific for the processing plant, species processed, and processing methods used. The record shall include:

1) the name and location of the processor or importer;

2) the date and time of the activity that the record reflects;

3) the signature or initials of the person performing the operation; and

4) where appropriate, the identity of the product and the production code, if any.  Processing and 	other information shall be entered at the time that it is observed.

The review of critical control point records shall occur within 1 week of the day that the records are made.

Any corrective actions shall be documented in a corrective action report.

Authors

Thomas E. Rippen (Seafood Technology Specialist), Sea Grant Extension Program

University of Maryland Eastern Shore, Princess Anne, MD  21853

and

Pamela D. Tom (Seafood Extension Program Manager)

Sea Grant Extension Program, University of California, Davis, CA 95616

UCSGEP 04-7W;  April 2004

This work is sponsored in part by NOAA, National Sea Grant College Program, Department of Commerce, under grant number NA04OAR4170038, project number A/EA-1, through the California Sea Grant College Program, and in part by the California State Resources Agency. The U.S. Government is authorized to reproduce and distribute reprints for governmental purposes.